## Slide 1: Embedded Linux Landscape
Day 1 • Session 4 • 30 minutes
Where Yocto fits in the ecosystem

## Slide 2: Session Agenda
1. The embedded Linux problem
2. Buildroot vs Yocto — the two main contenders
3. When to pick which
4. Cross-compilation fundamentals
5. Toolchain, sysroot, ABI, target triples

## Slide 3: The Embedded Linux Problem
Why we can't just 'apt install' our way to an embedded device.
Desktop Linux assumes
• Lots of RAM, lots of disk
• A package manager with network access
• Generic x86_64 hardware
• Someone is sitting at a keyboard
Embedded Linux reality
• Tight resources — 256 MB RAM, 1 GB flash is common
• Custom hardware — ARM SoC, specific peripherals
• Headless — no keyboard, often no display
• Cross-compiled — build on x86, run on ARM
• Customer-shipped — must be reproducible, supportable for years
So we need a build system that handles all of this end to end. That's where Buildroot and Yocto come in.

## Slide 4: Buildroot vs Yocto
Both are popular. They make different trade-offs.
Buildroot
Philosophy
Make + Kconfig. Simple. Linear.
Strengths
• Easy to learn
• Faster first build
• Small images out of the box
• Good for one product, one team
Limits
• No layering / per-vendor reuse
• Hard to scale across many products
• Incremental builds less robust
Yocto
Philosophy
BitBake + layered metadata. Powerful. Steep.
Strengths
• Layers — vendor BSP + your product + community
• sstate cache — fast incremental builds
• SBOM, license, CVE tooling built in
• Industry standard
Limits
• Steeper learning curve
• Larger disk and RAM needs
• Slower first build

## Slide 5: When To Pick Which
Match the tool to the problem, not the fashion.
Pick Buildroot when
• One product, one team
• Short product lifetime
• Image size is the dominant constraint
• Team has no Yocto experience and timeline is tight
• Hobbyist / prototype work
Real example
A simple sensor node with one MCU running Linux, sold in low volume.
Pick Yocto when
• Multiple products sharing a code base
• 5+ year product lifetime
• Compliance pressure (license, CVE, SBOM)
• Vendor ships a BSP as a meta-layer
• Need to support multiple hardware variants
Real example
A medical device family — one base image, three hardware variants, 10-year support.

## Slide 6: Cross-Compilation Fundamentals
Build on one machine, run on another. The standard for embedded.
Host vs target
Host = your build machine (typically x86_64 Linux)
Target = the device you're building for (typically ARM)
What a cross-toolchain provides
• Cross-compiler (e.g., arm-linux-gnueabihf-gcc)
• Cross-binutils (as, ld, objdump for the target)
• Target sysroot — libraries and headers the target will use
Yocto generates the toolchain for you
You don't install one separately. Yocto builds gcc + binutils + glibc against your target's spec, fresh every time it changes.

## Slide 7: Triples and ABIs
How toolchains identify which target they're for.
A target triple has 3 or 4 parts: arch-vendor-os-abi
# Common triples
x86_64-linux-gnu # 64-bit x86 desktop
aarch64-linux-gnu # 64-bit ARM (most modern SoCs)
arm-linux-gnueabi # 32-bit ARM, soft-float ABI
arm-linux-gnueabihf # 32-bit ARM, hard-float ABI
armv7-linux-musleabihf # 32-bit ARMv7, musl libc, hard-float
# What the parts mean
# arch = CPU family + sometimes version (armv7, aarch64)
# vendor = often omitted or 'linux'
# os = linux, none, mingw32, ...
# abi = gnu (glibc), gnueabihf, musl, ...
Mixing ABIs is the #1 source of weird linker errors. armv7-eabi binaries don't run on eabihf systems and vice versa.

## Slide 8: Session Summary
5 things to remember from this session.
1
Embedded Linux needs a real build system, not apt-install
Cross-compile, fit constraints, ship a fixed image
2
Buildroot is simpler; Yocto is more powerful
Pick based on product lifetime, team size, compliance needs
3
Yocto wins when you have multiple products or long lifetimes
Layering + sstate + compliance tools pay off at scale
4
Cross-compilation = build on host, run on target
Yocto handles toolchain generation for you
5
Target triples identify the binary ABI
Mixing them quietly causes the strangest bugs
Next session → Yocto Architecture (75 min) — Poky, BitBake, recipes, layers, sstate