## Slide 1: BSP and Kernel Integration
Day 2 • Session 4 • 75 minutes
Hardware enablement, kernel recipes, device tree, config fragments

## Slide 2: Session Agenda
1. BSP layer structure — meta-bsp vs meta-product
2. MACHINE tuning — CPU features, boot args, storage
3. Kernel recipe strategy — vendor fork vs mainline
4. Device tree workflow
5. Kernel configuration fragments
6. Building and inspecting the kernel

## Slide 3: BSP Layer Design
Split hardware-specific stuff from product-specific stuff.
meta-yourbsp
Purpose
Enable the hardware. Nothing else.
Contents
• MACHINE config files
• Kernel recipe / bbappend
• Bootloader recipe
• Device tree sources
• Firmware blobs
• Hardware-specific drivers
Reused
Across all products on this hardware
meta-yourproduct
Purpose
Your application logic, branding, business rules.
Contents
• Application recipes
• Custom systemd units
• Branding (splash, hostname)
• Image recipes
• Per-product DT overlays
• Customer-specific configs
Reused
Just for this product line
Why split? When you ship a new product on the same hardware, only meta-yourproduct changes.

## Slide 4: MACHINE Tuning
What goes into your machine config file.
# meta-yourbsp/conf/machine/yourboard.conf
# Inherit a common tuning include for ARMv8
require conf/machine/include/arm/armv8a/tune-cortexa72.inc
# Kernel and bootloader providers
PREFERRED_PROVIDER_virtual/kernel = "linux-yocto"
PREFERRED_PROVIDER_virtual/bootloader = "u-boot"
# Device tree to use
KERNEL_DEVICETREE = "vendor/yourboard.dtb"
# What this hardware can do
MACHINE_FEATURES = "usbhost ethernet wifi bluetooth alsa"
# Boot arguments
APPEND += "root=/dev/mmcblk0p2 rootwait console=ttyS0,115200"
# Image format for flashing
IMAGE_FSTYPES += "wic.bz2"
WKS_FILE = "yourboard.wks"

## Slide 5: Kernel Recipe Strategy
Three approaches. Pick based on what your SoC vendor provides.
linux-yocto
Yocto's curated kernel
What:
Yocto's reference
kernel with BSP
branches
Use when:
Mainstream HW with
linux-yocto BSP
support (RPi, BBB,
some i.MX)
linux-yocto-rt
Real-time variant
What:
linux-yocto +
PREEMPT_RT patches
Use when:
Real-time latency
requirements:
industrial control,
robotics, audio
vendor kernel
Vendor BSP fork
What:
Vendor's own fork
(NXP, TI, Xilinx, etc.)
Use when:
SoC vendor only
supports their fork,
or you need their
out-of-tree drivers
Reality: most products use the vendor BSP kernel because that's where the drivers live.

## Slide 6: Device Tree Workflow
Describe hardware to the kernel without compiling code.
# Where DT sources live:
# In the kernel tree: arch/arm64/boot/dts/<vendor>/<board>.dts
# Plus any overlays: arch/arm64/boot/dts/<vendor>/<board>-feature.dtbo
# Yocto wires it up via KERNEL_DEVICETREE:
KERNEL_DEVICETREE = "vendor/yourboard.dtb vendor/yourboard-feature.dtbo"
# To add a DT overlay from your meta-product layer:
# meta-yourproduct/recipes-kernel/linux/linux-yocto.bbappend:
FILESEXTRAPATHS:prepend := "${THISDIR}/files:"
SRC_URI += "file://yourproduct-leds.dts"
# Then a do_compile prepend or kernel-devicetree class handles the .dtb
# Inspect the loaded DT on a running device:
ls /sys/firmware/devicetree/base/
dtc -I fs -O dts /sys/firmware/devicetree/base

## Slide 7: Kernel Config Fragments
Don't edit .config by hand. Layer your changes as fragments.
# Why fragments beat a hand-edited defconfig:
# - Composable: add fragments per feature or per machine
# - Reviewable: smaller diffs
# - Maintainable: kernel upgrades don't lose your changes
# Example fragment: meta-yourproduct/recipes-kernel/linux/files/myfeatures.cfg
CONFIG_USB_SERIAL_FTDI_SIO=y
CONFIG_I2C_CHARDEV=y
CONFIG_GPIO_SYSFS=y
# Wire it up via bbappend:
# meta-yourproduct/recipes-kernel/linux/linux-yocto.bbappend
FILESEXTRAPATHS:prepend := "${THISDIR}/files:"
SRC_URI += "file://myfeatures.cfg"
# Build and verify:
# bitbake virtual/kernel -c menuconfig (interactive)
# After boot: zcat /proc/config.gz | grep USB_SERIAL_FTDI

## Slide 8: Building and Inspecting
Commands to know for kernel work.
# Build just the kernel
bitbake virtual/kernel
# Find the kernel deploy artifacts
ls tmp/deploy/images/${MACHINE}/ | grep -E '(Image|zImage|bzImage|dtb)'
# Drop into menuconfig (experimental — changes won't stick)
bitbake virtual/kernel -c menuconfig
# After menuconfig, save your edits as a fragment
bitbake virtual/kernel -c diffconfig
# Look at fragment.cfg printed by the previous command
# Drop into a devshell for kernel source debugging
bitbake virtual/kernel -c devshell
# Inside, you have the kernel source as if you were doing a make build
# Force a clean rebuild
bitbake virtual/kernel -c cleansstate
bitbake virtual/kernel

## Slide 9: Session Summary
5 things to remember from this session.
1
Split hardware (meta-bsp) from product (meta-product)
Saves you when you re-use hardware across products
2
Machine config wires kernel, bootloader, DT, features, image format
One file ties hardware to Yocto
3
Three kernel strategies — vendor fork is most common in practice
linux-yocto for community-supported HW; vendor for SoC-specific drivers
4
Device tree describes hardware without code
Edit .dts, recompile to .dtb; kernel uses it at boot
5
Config fragments layer kernel changes
Never hand-edit defconfig — fragments survive kernel upgrades
Next session → Build Debugging (60 min) — diagnosing failures fast