## Slide 1: Device Tree Debugging
Day 3 • Session 3 • 60 minutes
Diagnose bring-up issues fast

## Slide 2: Session Agenda
1. DT recap — what it is, what it does
2. Where to look on a running system
3. EPROBE_DEFER — Linux's retry mechanism
4. Five common failure modes
5. Pre-recorded failure scenarios — walkthrough
6. Debug cheat sheet

## Slide 3: DT Recap
Quick refresher before we go debugging.
Device tree describes hardware to the kernel
Without it, the kernel would need code for every board. With it, the same kernel boots many boards.
Anatomy
• Nodes — components (cpu, i2c, gpio, ...)
• Properties — key/value attributes of a node
• compatible — string matching a driver
• reg — memory-mapped address
• status — disabled vs okay
• phandle/references — link nodes (e.g., to a clock)
The driver binding model
Driver advertises a compatible string. Kernel finds a node with matching compatible. Driver's probe() is called.

## Slide 4: Where to Look on a Running System
Four interfaces, listed in order of usefulness.
# 1. The live DT as the kernel sees it
ls /sys/firmware/devicetree/base/
# Each subdirectory is a node; files inside are properties
# Decompile the live tree back to DTS for reading
dtc -I fs -O dts /sys/firmware/devicetree/base > live.dts
less live.dts
# 2. Boot messages — what bound, what didn't
dmesg | grep -i 'device tree'
dmesg | grep -E 'probe|defer'
# 3. What's bound to a driver
ls /sys/bus/platform/devices/
ls /sys/bus/i2c/devices/
ls /sys/class/leds/
# 4. Drivers waiting for dependencies
cat /sys/kernel/debug/devices_deferred
# Lists drivers stuck in EPROBE_DEFER

## Slide 5: EPROBE_DEFER — Linux's Retry Loop
Why drivers seem to 'not bind' but actually retry.
The pattern
A driver's probe() may need a clock, regulator, or GPIO that isn't ready yet.
Instead of failing, it returns -EPROBE_DEFER.
Kernel retries periodically as other drivers initialize.
What you see
• Driver doesn't appear in dmesg as 'bound'
• Device shows up under /sys/devices/platform/
• But /sys/class/<type>/ stays empty
What to check
cat /sys/kernel/debug/devices_deferred
That tells you the device is waiting on something. Look upstream in the DT to find what it depends on (clocks, resets, regulators).

## Slide 6: Five Common Failure Modes
The bugs that hit 80% of bring-up sessions.
1
Wrong compatible string
Driver loads but doesn't bind. Check Documentation/devicetree/bindings/.
2
Missing or wrong reg
Driver probes but reads garbage / triggers fault. Check SoC reference manual.
3
Missing clocks or resets
Driver returns EPROBE_DEFER forever. /sys/kernel/debug/devices_deferred shows it.
4
GPIO conflict between nodes
Two nodes claim the same GPIO; second to probe fails. Check pinctrl assignments.
5
status = "disabled"
Node is in the DT but kernel ignores it. Change to status = "okay" or add overlay.

## Slide 7: Failure Scenario 1 — Walkthrough
GPIO LED node added; driver loads but no LED appears.
# Your DT overlay snippet
status_led: status-led {
compatible = "gpio-leds";
led-0 {
gpios = <&gpio 17 0>;
default-state = "off";
};
};
# After boot — no LED in /sys/class/leds/
ls /sys/class/leds/
# (empty or missing your led)
# Check dmesg
dmesg | grep -i -E 'gpio-leds|led'
# → 'gpio-leds: probe failed with -EBUSY'
# Diagnosis: GPIO 17 is already claimed by another driver
cat /sys/kernel/debug/gpio
# Look for 'gpio-17' — whatever holds it is the conflict
# Fix: pick a free GPIO, or disable the conflicting node

## Slide 8: Failure Scenario 2 — Walkthrough
I2C sensor in DT, kernel shows nothing under i2c bus.
# Your DT node
&i2c1 {
sensor: bme280@76 {
compatible = "bosch,bme280";
reg = <0x76>;
};
};
# After boot — sensor doesn't appear
ls /sys/bus/i2c/devices/
# (no entry)
# Check that i2c1 is enabled
cat /sys/firmware/devicetree/base/soc/i2c@*/status
# May show 'disabled'
# Diagnosis: i2c1 is disabled at the SoC level
# Fix: enable i2c1 in your overlay
&i2c1 {
status = "okay";
// ... sensor node here
};

## Slide 9: Failure Scenario 3 — Walkthrough
Driver returns EPROBE_DEFER forever — missing clock.
# Check what's deferred
cat /sys/kernel/debug/devices_deferred
# Output:
# 11000000.serial serial8250-of
# This serial port driver is stuck waiting for something
dmesg | grep 11000000.serial
# → 'failed to get clock'
# Look at the DT node for that device
cat /sys/firmware/devicetree/base/soc/serial@11000000/clocks
# Should reference a phandle to a clock provider
# Diagnosis: the clock provider node has status='disabled'
# or the phandle in 'clocks' points to a non-existent node
# Fix: enable the clock controller in DT, or fix the phandle reference

## Slide 10: Debug Cheat Sheet
Print this. Keep it on your desk.
# WHAT BOUND, WHAT DIDN'T
ls /sys/bus/platform/devices/ # all platform devices
ls /sys/class/ # bound by class (leds, gpio, etc.)
cat /sys/kernel/debug/devices_deferred
# WHAT THE KERNEL SAID DURING BOOT
dmesg | grep -i -E 'probe|defer|device tree|of_'
# THE LIVE TREE
dtc -I fs -O dts /sys/firmware/devicetree/base | less
# A SPECIFIC NODE
find /sys/firmware/devicetree/base/ -name 'serial*' -type d
ls /sys/firmware/devicetree/base/soc/serial@11000000/
cat /sys/firmware/devicetree/base/soc/serial@11000000/compatible
# GPIO USAGE
cat /sys/kernel/debug/gpio
# I2C USAGE
ls /sys/bus/i2c/devices/
i2cdetect -y 1 # scan i2c-1 for addresses

## Slide 11: Session Summary
5 things to remember from this session.
1
Read the live tree first
/sys/firmware/devicetree/base is the truth; dtc decompiles it back to DTS
2
EPROBE_DEFER is not an error
It's the kernel saying 'not ready yet'; look at devices_deferred
3
Five common failures cover most cases
compatible, reg, clocks/resets, GPIO conflicts, status=disabled
4
dmesg + /sys + /sys/kernel/debug = your toolkit
Three places give 95% of the information you need
5
DT bugs are hardware-specific
Don't fix in software what's wrong in the DT — fix the DT
Next session → Bootloader Overview (30 min)