## Slide 1: Performance on Target
Day 4 • Session 5 • 75 minutes
Boot time, memory, CPU, IO

## Slide 2: Session Agenda
1. Boot time — measure with systemd-analyze
2. Boot time — common levers and what each gives you
3. Memory footprint — free, smem, ps
4. CPU utilization — top, mpstat, perf
5. I/O bottlenecks — iotop, iostat
6. Hands-on measurement on TrainerGW

## Slide 3: Boot Time — Measurement
First, know what you're optimizing.
# Overall boot time
systemd-analyze
# Startup finished in 1.234s (kernel) + 5.678s (userspace) = 6.912s
# multi-user.target reached after 5.678s in userspace.
# What took longest in userspace
systemd-analyze blame
# 2.341s nginx.service
# 1.234s NetworkManager.service
# 0.876s systemd-journal-flush.service
# ...
# Critical chain — what's actually blocking boot completion
systemd-analyze critical-chain
# Render a visual SVG plot
systemd-analyze plot > boot.svg
# View on host with a browser
# Kernel-side timing per initcall
# Add 'initcall_debug' to bootargs in U-Boot
# Then on boot:
dmesg | grep 'initcall.*took'
dmesg | awk '/initcall.*took/ {print $NF, $0}' | sort -n | tail

## Slide 4: Boot Time — Common Levers
What each lever gives you on a typical device.
Lever 1: Disable services you don't need
systemctl disable <service> — savings: 0.5–3 seconds depending on service
Lever 2: Strip kernel debug info
CONFIG_DEBUG_INFO=n, CONFIG_DEBUG_INFO_DWARF_TOOLCHAIN_DEFAULT=n — kernel ~50% smaller, ~50–100 ms faster
Lever 3: Drop initramfs if you can
Mount rootfs directly — savings: 200–500 ms (depending on initramfs size)
Lever 4: quiet boot + earlycon
bootargs += "quiet loglevel=4 earlycon" — saves serial I/O time, 100–200 ms typical
Lever 5: Replace bash with dash for early scripts
In Yocto: VIRTUAL-RUNTIME_base-utils-syslog = "dash"; init scripts much faster

## Slide 5: Memory Footprint
What's using your RAM, and is it justified?
# Overall
free -h
# total used free shared buff/cache available
# Mem: 992Mi 240Mi 450Mi 2.0Mi 302Mi 700Mi
# Per-process (sorted by RSS)
ps aux --sort=-rss | head
# Same but more accurate — accounts for shared pages
smem -k -s pss -r | head
# PID User Command Swap USS PSS RSS
# 1234 root /usr/bin/python3 my_daemon 0 15.4M 18.2M 25.6M
# Kernel memory
cat /proc/meminfo | grep -E '^(MemTotal|MemFree|Slab|KernelStack|PageTables)'
# What's allocating most slab
cat /proc/slabinfo | sort -k 3 -nr | head

## Slide 6: CPU Utilization
Find what's actually using your cores.
# Live, sorted by CPU%
top
# Press 'P' to sort by CPU, '1' to see per-core
# Per-process, no UI
ps aux --sort=-%cpu | head
# Per-core utilization (need sysstat package)
mpstat -P ALL 2
# What's actually waiting on what
vmstat 2
# Look at 'r' (runnable) and 'b' (blocked) columns
# Profile a specific process
perf top -p <pid>
perf record -p <pid> -g sleep 10
perf report
# What syscalls are slow
strace -c -p <pid>
# Press Ctrl-C; see syscall summary

## Slide 7: I/O Bottlenecks
Disk I/O is often the hidden killer on embedded.
# Per-process I/O activity (sysstat or iotop)
iotop
# Press 'o' to show only processes currently doing I/O
iotop -a -d 5
# Device-level
iostat -x 2
# rkB/s wkB/s await %util
# mmcblk0p2 0.50 25.4 8.20 45.2%
# Open files per process
lsof -p <pid> | head
# Filesystem-level — what's slow
filetop # (if bpftrace/perf-tools installed)
# Common I/O issues on embedded:
# - Frequent fsync calls (sqlite default) — batch them or use WAL mode
# - Lots of small writes to same dir — block-level pressure
# - readahead too aggressive on flash — tune in /sys/block/.../queue/read_ahead_kb

## Slide 8: Hands-On Measurement
Apply the tools to TrainerGW. Find one thing to fix.
# Boot TrainerGW and run the lab
# 1. Measure boot
systemd-analyze
systemd-analyze blame | head -10
systemd-analyze critical-chain
# 2. Identify the slowest service. Investigate why.
systemctl status <slow-service>
journalctl -u <slow-service>
# 3. Memory snapshot
free -h
ps aux --sort=-rss | head
# 4. CPU under load — generate some
yes > /dev/null &
yes > /dev/null &
top # observe; pkill yes when done
# 5. I/O test
dd if=/dev/zero of=/tmp/iotest bs=1M count=100 conv=fdatasync
iostat -x 2 5 &
dd if=/dev/zero of=/tmp/iotest bs=1M count=100 conv=fdatasync
# 6. Optional: apply one optimization and re-measure

## Slide 9: Session Summary
5 things to remember from this session.
1
systemd-analyze is the start of boot-time work
Overall, blame, critical-chain, plot — four commands cover most of it
2
Five common boot-time levers give cumulative savings
Disable services, strip kernel debug, drop initramfs, quiet boot, dash
3
Memory: free + smem give different but useful views
Use smem for accurate per-process accounting (PSS vs RSS)
4
CPU profiling = top + perf
top tells you who; perf tells you what they're doing
5
I/O is often the hidden cost
iotop + iostat to find culprits; usually fsync-heavy apps or SD card stalls
Next session → Updating and Maintaining Devices (45 min)