## Slide 1: Boot, Flash, Verify
From image artifact to a working device

## Slide 2: Session Agenda
1. Boot flow on a real device
2. Flashing — wic, sdcard, raw partitions
3. First-boot checklist
4. Common bring-up failures
5. Validating the boot was clean

## Slide 3: Boot Flow on a Real Device
What happens between power and login.
Power
Reset
ROM
Vendor
SPL
Stage 1
U-Boot
Stage 2
Kernel
Init HW
initramfs
Mount /
systemd
Services
login
Ready
Stages to remember
• Vendor ROM (BootROM): vendor's first-stage; usually unmodifiable
• SPL: minimal loader that brings up DRAM and loads U-Boot
• U-Boot: loads kernel + DTB + initramfs; passes bootargs
• Kernel: initializes hardware, mounts root filesystem
• systemd: starts services per unit dependencies
If boot fails, identify which stage. The fix lives in that stage.

## Slide 4: Flashing Methods
Three common paths from .wic to a bootable device.
bmaptool
Faster than dd
When:
WIC images with
.bmap files
Skips unallocated blocks
Command:
bmaptool copy \
image.wic.bz2 /dev/sdX
Typical for SD cards
dd
Universal fallback
When:
Everywhere
Works with any image
type and any target
Command:
sudo dd if=img.wic \
of=/dev/sdX bs=4M \
status=progress
Slower than bmaptool
vendor flasher
SoC-specific
When:
Specific SoC vendor
tools
Examples:
• uuu (NXP i.MX)
• mfgtool (NXP)
• rkdeveloptool (Rockchip)
• STM32CubeProgrammer
Required for some

## Slide 5: First-Boot Checklist
What to verify in the first 60 seconds after powering on.
# 1. Did we even boot? Check serial console.
# Should see kernel messages and a login prompt.
# 2. Time and date sane?
date
# If off, NTP didn't start, or RTC is missing/broken
# 3. Network up?
ip addr show
ping -c 2 8.8.8.8
# 4. All filesystems mounted?
df -h
# Look for / and /data (or whatever your layout uses)
# 5. CPU and memory healthy?
free -h
cat /proc/loadavg
# 6. Any kernel errors or warnings?
dmesg --level=err,warn
# 7. systemd happy?
systemctl --failed
systemctl is-system-running

## Slide 6: Common Bring-Up Failures
What goes wrong on first boot — and what to look at.
1
Stuck at U-Boot prompt
Kernel/DTB not found at expected path. Check bootargs and partition mounts in U-Boot.
2
Kernel panics on mount root
rootfstype, root path wrong, or rootwait missing. Inspect APPEND.
3
Black screen, no serial output
Wrong console= argument; or earlycon not enabled. Check cmdline.
4
Boots but no network
Driver missing, MAC not set, no DHCP. Check dmesg, ip link, journalctl -u systemd-networkd.
5
systemd hangs forever
Failed dependency, missing service file, or bad mount. Try systemd.debug-shell=1.

## Slide 7: Validating a Clean Boot
Beyond 'it booted' — what does 'clean' actually mean?
# Clean boot checklist
# No failed units
systemctl --failed
# Output should be: '0 loaded units listed.'
# No kernel errors or warnings
dmesg --level=err,warn
# Should be empty or only known-acceptable lines
# Boot completed within target time
systemd-analyze
systemd-analyze blame | head -10
# All expected services running
systemctl status nginx hello-trainergw chronyd
# Verify CVE/SBOM artifacts are present
ls /usr/share/common-licenses/ 2>/dev/null | head
test -f /etc/os-release && cat /etc/os-release
# Confirm no unexpected processes (Yocto images are minimal)
ps aux | wc -l

## Slide 8: Session Summary
5 things to remember from this session.
1
Boot has stages; bug fixes live in the right stage
ROM → SPL → U-Boot → Kernel → initramfs → systemd → login
2
Three flash methods cover almost any device
bmaptool fastest; dd universal; vendor tool for special SoCs
3
First-boot checklist is ~7 commands
date, ip, df, free, dmesg, systemctl --failed — 60 seconds total
4
Common failures cluster around 5 patterns
Boot args, root mount, console, network init, systemd deps
5
'Clean boot' is verifiable, not vibes
No failed units, no kernel errors, expected boot time, all services up
Next session → Day-to-day operations