## Slide 1: Recipes: Part 2
Packaging and image composition

## Slide 2: Session Agenda
1. Packaging models — rpm, deb, ipk
2. Selection criteria for embedded products
3. IMAGE_FEATURES — what they actually do
4. Packagegroups — bundling related software
5. IMAGE_INSTALL patterns
6. Distro features vs machine features vs image features

## Slide 3: Three Packaging Models
Yocto can produce any of three package formats. Pick one.
ipk
Small embedded default
Origin: OpenWrt
Pros:
• Smallest overhead
• Fast on-target install
• Designed for embedded
Use when:
Most embedded products, especially when ipk feeds or opkg are involved
deb
Debian-derived prod
Origin: Debian/Ubuntu
Pros:
• Familiar to Debian devs
• Strong dependency support
• Wide tooling
Use when:
Your team comes from Debian/Ubuntu and you want apt-like workflows
rpm
Large/enterprise
Origin: Red Hat
Pros:
• Rich metadata, signing
• Default in Poky
• Mature tooling
Use when:
Compliance-heavy environments, RPM-based corporate infrastructure
Set in local.conf: PACKAGE_CLASSES = "package_ipk" (or _deb / _rpm). Default is rpm.

## Slide 4: Selection Criteria
How to actually choose between them for a real product.
Pick ipk if
• Image size matters (every MB counts)
• You need fast on-target package install/update
• You'll use opkg feeds for OTA package updates
Pick deb if
• Your team's muscle memory is apt
• You're already shipping Debian on devices and want continuity
Pick rpm if
• Your infrastructure (Spacewalk, Satellite, etc.) is RPM-native
• Compliance/signing matters more than size
• You don't mind the overhead
Cannot decide?
Use ipk. It's the safe default for almost any embedded product.

## Slide 5: IMAGE_FEATURES Pre-Packaged Personalities
Named sets of capabilities added to your image with one line.
# In your image recipe or local.conf
IMAGE_FEATURES += "debug-tweaks ssh-server-openssh package-management"
# Common features:
# debug-tweaks - empty root password, easy debug
# ssh-server-openssh - run sshd
# ssh-server-dropbear - run dropbear (lighter)
# tools-debug - gdb, strace, etc
# tools-sdk - dev tools on target
# x11-base - X server
# nfs-server, splash, eclipse-debug, dev-pkgs, doc-pkgs
# package-management - dnf/apt/opkg in the rootfs
# IMAGE_FEATURES vs EXTRA_IMAGE_FEATURES:
# IMAGE_FEATURES → typically set in the image recipe
# EXTRA_IMAGE_FEATURES → typically set in local.conf (user-level)

## Slide 6: Packagegroups: Bundling
Group related software into one name; install or remove together.
# A packagegroup recipe in your layer:
# meta-trainerdemo/recipes-core/packagegroups/packagegroup-trainergw-core.bb
SUMMARY = "Core packages for TrainerGW image"
PACKAGE_ARCH = "${MACHINE_ARCH}"
inherit packagegroup
RDEPENDS:${PN} = "\
nginx \
hello-trainergw \
systemd-analyze \
chrony \
iptables \
"
# Use it in your image:
IMAGE_INSTALL:append = " packagegroup-trainergw-core"

## Slide 7: Distro vs Machine vs Image
Three overlapping but distinct lists. Know which to use.
DISTRO_FEATURES
Distro-level capabilities
What the OS can do
Examples:
wifi, bluetooth, opengl,
x11, ipv6, alsa, pam
Set in distro conf
Affects which recipes
and PACKAGECONFIG
options are picked
MACHINE_FEATURES
Hardware capabilities
What the board has
Examples:
usbhost, ethernet, wifi,
bluetooth, screen, alsa
Set in machine conf
Affects what packages
make sense for this
hardware
IMAGE_FEATURES
Image-level personality
What this image bundles
Examples:
debug-tweaks, tools-debug,
ssh-server-openssh,
package-management
Set in image recipe or
local.conf
Affects this image only
Effective features = (DISTRO_FEATURES ∩ MACHINE_FEATURES) used by recipes, plus IMAGE_FEATURES for the image.

## Slide 8: Session Summary
5 things to remember from this session.
1
Three packaging formats — ipk is the safe default for embedded
Switch via PACKAGE_CLASSES; affects on-target install workflow
2
IMAGE_FEATURES are named bundles of capabilities
debug-tweaks, ssh-server-*, tools-debug, package-management are most-used
3
Packagegroups bundle related recipes
One name → many RDEPENDS → cleaner image recipes
4
DISTRO/MACHINE/IMAGE features are different lists
Distro = OS, Machine = hardware, Image = personality
5
Most product images compose all four
Distro features + Machine features + Packagegroup + IMAGE_INSTALL = your image
Next session → BSP and Kernel — Hardware enablement