## Slide 1: Bootloader Overview
U-Boot, EFI, GRUB — where kernel meets hardware

## Slide 2: Session Agenda
1. What a bootloader does
2. Three families — U-Boot, EFI, GRUB
3. When to use which
4. How Yocto handles bootloader config
5. Boot arguments — passing info to the kernel

## Slide 3: What a Bootloader Does
The bridge from power-on to a running kernel.
Power on
Reset vector
ROM code
Vendor first-stage
SPL
Second-stage loader
U-Boot
Full bootloader
Kernel
Linux takes over
What the bootloader actually does
• Init DRAM, clocks, basic peripherals
• Load the kernel image into RAM from flash/SD/eMMC/network
• Load the device tree blob (DTB)
• Pass boot arguments to the kernel
• Jump to the kernel entry point
From there, the kernel runs init, mounts the rootfs, starts systemd, and you have a system.

## Slide 4: Three Bootloader Families
Different problems, different tools.
U-Boot
Embedded king
What:
Configurable bootloader
with shell and scripts
Used on:
Most ARM SoCs
Most embedded products
Strengths:
Flexible, scriptable,
supports many storage
and network protocols
EFI / UEFI
x86/ARM server style
What:
Firmware spec, not a
single loader
Used on:
x86 desktops/servers,
newer ARM platforms,
RPi5 (optional)
Strengths:
Secure Boot,
standardized,
GPT partitioning
GRUB
Distro classic
What:
The Linux distro
bootloader
Used on:
x86 servers, full
desktop-like systems
Strengths:
Multi-OS boot menus,
filesystem support,
well-known

## Slide 5: When to Use Which
Match the loader to the platform.
Pick U-Boot when
• Custom ARM hardware
• Need flexible boot scripts (A/B updates, fallback)
• Need TFTP/NFS boot for dev
• Tight flash budgets
Typical example
i.MX, BeagleBone, custom industrial gateways
Pick EFI/GRUB when
• x86_64 hardware (server, intel NUC, etc.)
• Need Secure Boot certified by Microsoft
• Multi-OS boot or distro-style menus
• Lots of disk space, no flash constraints
Typical example
Edge servers, industrial PCs, infotainment

## Slide 6: Yocto Bootloader Wiring
How U-Boot config flows from machine.conf to flashed device.
# In meta-yourbsp/conf/machine/yourboard.conf
PREFERRED_PROVIDER_virtual/bootloader = "u-boot"
UBOOT_MACHINE = "yourboard_defconfig"
# U-Boot recipe is provided by Yocto or the BSP
# bitbake u-boot
# Output: tmp/deploy/images/${MACHINE}/u-boot.bin (or u-boot.imx, etc.)
# Boot arguments passed to kernel - define in machine.conf
APPEND += "root=/dev/mmcblk0p2 rootwait console=ttyS0,115200"
# WIC kickstart wires bootloader + kernel + rootfs into a flashable image
WKS_FILE = "yourboard.wks"
# yourboard.wks example:
# part u-boot --source rawcopy --sourceparams="file=u-boot.bin" --no-table
# part /boot --source bootimg-partition --align 4 --fixed-size 32M --fstype=vfat
# part / --source rootfs --fstype=ext4 --align 4

## Slide 7: Boot Arguments
How you tell the kernel about the device.
# Common boot args you'll set in APPEND or via U-Boot bootargs
console=ttyS0,115200 # where kernel prints (serial port)
root=/dev/mmcblk0p2 # where rootfs lives
rootwait # wait for storage to appear before mounting root
rootfstype=ext4
quiet # suppress most kernel messages
loglevel=4 # 0=silent, 7=verbose
earlycon # enable early console before normal one
ro # mount rootfs read-only initially
# For debugging:
initcall_debug # show every init call's timing
debug # very verbose
ignore_loglevel # show all kernel messages regardless of loglevel=
# View at runtime
cat /proc/cmdline

## Slide 8: Session Summary
5 things to remember from this session.
1
Bootloader connects firmware to Linux
Init hardware, load kernel + DT + initramfs, pass arguments, jump
2
Three families: U-Boot for embedded, EFI for x86, GRUB for distros
Pick by platform — U-Boot dominates ARM embedded
3
Yocto provides u-boot recipe, wires via machine.conf
PREFERRED_PROVIDER + UBOOT_MACHINE + WKS_FILE = end-to-end flash
4
Boot arguments live in APPEND
console, root, rootwait, loglevel — these four cover most needs
5
/proc/cmdline shows what booted
First thing to check when boot behavior looks wrong
Next session → Image Engineering - WIC, partitions, filesystems